## Slide 1
Introduction to IP Multicast
1
Cisco Systems Confidential
0810_04F7_c2

## Slide 2
Manoj Leelanivas
2
Cisco Systems Confidential
0810_04F7_c2
Software Engineer

## Slide 3
IP Multicast Technology and Concepts
IP Multicast Host-to-Router Protocols
IP Multicast Routing Protocols
Protocol Independent Multicast—PIM
General Multicast Concepts
Deliverables
Agenda

## Slide 4
Why multicast?
When sending same data to multiple receivers
Better bandwidth utilization
Lesser host/router processing
Receivers’ addresses unknown
Applications
Video/audio conferencing
Resource discovery/service advertisement
Stock distribution
Eg. Vat, Vic, IP/TV, Pointcast
Introduction to Multicast

## Slide 5
Unicast/Multicast
Host
Router
Unicast
Host
Router
Multicast

## Slide 6
RFC 1112
Each multicast group identified by a class-D IP address
Members of the group could be present anywhere in the Internet
Members join and leave the group and indicate this to the routers
Senders and receivers are distinct: i.e., a sender need not be a member
Routers listen to all multicast addresses and use multicast routing protocols to manage groups
IP Multicast Service Model

## Slide 7
IP Multicast Service Model (Cont.)
IP group addresses
Class D address—high-order 3 bits are set (224.0.0.0)
Range from 224.0.0.0 through 239.255.255.255
Well known addresses designated by IANA
Reserved use: 224.0.0.0 through 224.0.0.255
224.0.0.1—all multicast systems on subnet
224.0.0.2—all routers on subnet
Transient addresses, assigned and reclaimed dynamically
Global scope: 224.0.1.0-238.255.255.255
Limited Scope: 239.0.0.0-239.255.255.255
  Site-local scope: 239.253.0.0/16
  Organization-local scope: 239.192.0.0/14

## Slide 8
IP Multicast Service Model (Cont.)
Mapping IP group addresses to data-link multicast addresses
RFC 1112 defines OUI 0x01005e
Low-order 23-bits of IP address map into low-order 23-bits of IEEE address (eg. 224.2.2.2–01005e.020202)
Ethernet and FDDI use this mapping
Token Ring uses functional address-c000.4000.0000

## Slide 9
IP Multicast Service Model (Cont.)
Hosts
Routers
Host-to-Router Protocols (IGMP)
Multicast Routing Protocols (PIM)

## Slide 10
Internet Group Management Protocol—IGMP
How hosts tell routers about group membership
Routers solicit group membership from directly connected hosts
RFC 1112 specifies first version of IGMP
IGMP v2 and IGMP v3 enhancements
Supported on UNIX systems, PCs, and MACs
10
Cisco Systems Confidential
0810_04F7_c2

## Slide 11
Internet Group Management Protocol—IGMP
IGMP v1
Queries
Querier sends IGMP query messages to 224.0.0.1 with ttl = 1
One router on LAN is designated/elected to send queries
Query interval 60–120 seconds
Reports
IGMP report sent by one host suppresses sending by others
Restrict to one report per group per LAN
Unsolicited reports sent by host, when it first joins the group
11
Cisco Systems Confidential
0810_04F7_c2

## Slide 12
IGMP—Joining a Group
Host 1
Host 2
Host 3
Sends Report to 224.5.5.5
Sends Report to 224.2.0.1
Periodically Sends IGMP Query to 224.0.0.1
224.2.0.1
224.2.0.1 224.5.5.5
224.2.0.1

## Slide 13
IGMP v2:
Host sends leave message if it leaves the group and is the last member (reduces leave latency in comparison to v1)
Router sends G-specific queries to make sure there are no members present before stopping to forward data for the group for that subnet
Standard querier election
IGMP v3:
In design phase
Enables to listen only to a specified subset of the hosts sending to the group
Internet Group Management Protocol—IGMP

## Slide 14
IGMP—Leaving a Group
Host 1
Host 2
Host 3
Sends Leave for 224.5.5.5 to 224.0.0.2
Sends Leave for 224.2.0.1 to 224.0.0.2
Sends Group Specific IGMP Query to 224.2.0.1
224.2.0.1
Sends Report for 224.2.0.1
Sends Group Specific IGMP Query to 224.5.5.5
224.2.0.1
224.2.0.1

## Slide 15
Multicast Routing Protocols (Reverse Path Forwarding)
What is RPF?
A router forwards a multicast datagram if received on the interface used to send unicast datagrams to the source
B
C
A
F
Source
Receiver
Unicast
Multicast
D
E

## Slide 16
Multicast Routing Protocols (Reverse Path Forwarding)
If the RPF check succeeds, the datagram is forwarded
If the RPF check fails, the datagram is typically silently discarded
When a datagram is forwarded, it is sent out each interface in the outgoing interface list
Packet is never forwarded back out the RPF interface!

## Slide 17
Multicast Routing Protocols—Characteristics
Shortest Path or Source Distribution Tree
Receiver 1
B
E
A
D
F
Source
Notation: (S, G)
S = Source
G = Group
C
Receiver 2

## Slide 18
Multicast Routing Protocols—Characteristics
Shared Distribution Tree
Receiver 1
B
E
A
D (Shared Root)
F
Source 1
Notation: (*, G)
* = All Sources
G = Group
C
Receiver 2
Source 2

## Slide 19
Distribution trees
Source tree
Uses more memory O(S x G) but you get optimal paths from source to all receivers, minimizes delay
Shared tree
Uses less memory O(G) but you may get suboptimal paths from source to all receivers, may introduce extra delay
Protocols
PIM, DVMRP, MOSPF, CBT
Multicast Routing Protocols—Characteristics

## Slide 20
Multicast Routing Protocols—Characteristics
Types of multicast protocols
Dense-mode
  Broadcast and Prune behavior
  Similar to Radio broadcast
Sparse-mode
  Explicit Join behavior
  Similar to Pay Per View

## Slide 21
Multicast Routing Protocols—Characteristics
Dense-mode protocols
Assumes dense group membership
Branches that are pruned don’t get data
Pruned branches can later be grafted to reduce join latency
DVMRP—Distance Vector Multicast Routing Protocol
Dense-mode PIM—Protocol Independent Multicast

## Slide 22
Multicast Routing Protocols—Characteristics
Sparse-mode protocols
Assumes group membership is sparsely populated across a large region
Uses either source or shared distribution trees
Explicit join behavior—assumes no one wants the packet unless asked
Joins propagate from receiver to source or Rendezvous Point (Sparse mode PIM) or Core (Core-Based Tree)

## Slide 23
Broadcast and prune ideal for dense groups
Source trees created on demand based on RPF rule
If the source goes inactive, the tree is torn down
Easy plug-and-play
Draft: draft-ietf-idmr-pim-dense-spec-00.txt
Dense Mode PIM

## Slide 24
Branches that don’t care for data are pruned
Grafts to join existing source tree
Uses Asserts to determine forwarder for multi-access LAN
Prunes on non-RPF P2P links
Rate-limited prunes on RPF P2P links
Dense Mode PIM

## Slide 25
Dense Mode PIM Example
Source
Receiver 2
Receiver 1
D
F
I
B
C
A
E
G
H
Link
Data
Control
25
Cisco Systems Confidential
0810_04F7_c2

## Slide 26
Dense Mode PIM Example
Initial Flood of Data and Creation of State
Source
Receiver 2
Receiver 1
D
F
I
B
C
A
E
G
H
26
Cisco Systems Confidential
0810_04F7_c2

## Slide 27
Dense Mode PIM Example
Prune to Non-RPF Neighbor
Source
Prune
Receiver 2
Receiver 1
D
F
I
B
C
A
E
G
H
27
Cisco Systems Confidential
0810_04F7_c2

## Slide 28
Dense Mode PIM Example
C and D Assert to Determine Forwarder for the LAN, C Wins
Source
Asserts
Receiver 2
Receiver 1
D
F
I
B
C
A
E
G
H
28
Cisco Systems Confidential
0810_04F7_c2

## Slide 29
Dense Mode PIM Example
I Gets Pruned
E’s Prune is Ignored
G’s Prune is Overridden
Source
Prune
Receiver 2
Receiver 1
Join Override
Prune
D
F
I
B
C
A
E
G
H
29
Cisco Systems Confidential
0810_04F7_c2

## Slide 30
Dense Mode PIM Example
Source
Graft
Receiver 2
Receiver 3
Receiver 1
New Receiver, I Sends Graft
D
F
I
B
C
A
E
G
H
30
Cisco Systems Confidential
0810_04F7_c2

## Slide 31
Dense Mode PIM Example
Source
Receiver 2
Receiver 3
Receiver 1
D
F
I
B
C
A
E
G
H
31
Cisco Systems Confidential
0810_04F7_c2

## Slide 32
Explicit join model
Receivers join to the Rendezvous Point (RP)
Senders register with the RP
Data flows down the shared tree and goes only to places that need the data from the sources
Last hop routers can join source tree if the data rate warrants by sending joins to the source
RPF check for the shared tree uses the RP
RPF check for the source tree uses the source
Sparse Mode PIM

## Slide 33
Only one RP is chosen for a particular group
RP statically configured or dynamically learned (Auto-RP, PIM v2 candidate RP advertisements)
Data forwarded based on the source state (S, G) if it exists, otherwise use the shared state (*, G)
Draft: draft-ietf-idmr-pim-sm-spec-10.txt (soon to be RFC)
Draft: draft-ietf-idmr-pim-arch-04.txt
Sparse Mode PIM

## Slide 34
Sparse Mode PIM Example
Receiver 1
B
E
A
D
Source
C
Receiver 2
RP
Link
Data
Control

## Slide 35
Sparse Mode PIM Example
Receiver 1
B
E
A
D
Source
Receiver 1 Joins Group G C Creates (*, G) State, Sends (*, G) Join to the RP
C
Receiver 2
RP
Join

## Slide 36
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
RP Creates (*, G) State
C
Receiver 2

## Slide 37
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
Source Sends Data A Sends Registers to the RP
C
Receiver 2
Register

## Slide 38
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
RP De-Encapsulates Registers Forwards Data Down the Shared Tree Sends Joins Towards the Source
C
Receiver 2
Join
Join

## Slide 39
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
RP Sends Register-Stop Once Data Arrives Natively
C
Receiver 2
Register-Stop

## Slide 40
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
C Sends (S, G) Joins to Join the Shortest Path (SPT) Tree
C
Receiver 2
(S, G) Join

## Slide 41
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
When C Receives Data Natively, It Sends Prunes Up the RP tree for the Source. RP Deletes (S, G) OIF and Sends Prune Towards the Source
C
Receiver 2
(S, G) RP Bit Prune
(S, G) Prune

## Slide 42
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
New Receiver 2 Joins E Creates State and Sends (*, G) Join
C
Receiver 2
(*, G) Join

## Slide 43
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
C Adds Link Towards E to the OIF List of Both (*, G) and (S, G) Data from Source Arrives at E
C
Receiver 2

## Slide 44
Sparse Mode PIM Example
Receiver 1
B
E
A
RP
D
Source
New Source Starts Sending D Sends Registers, RP Sends Joins RP Forwards Data to Receivers through Shared Tree
C
Receiver 2
Source 2
Register

## Slide 45
TTL scoping
To keep multicast traffic within an administrative domain by setting ttl thresholds on interfaces on the border router
Administratively scoped addresses
A multicast boundary can be setup on the borders for addresses in range of 239.0.0.0–239.255.255.255
Better than ttl scoping (pruning, solid wall)
Multicast Features: Multicast Scope Control
45
Cisco Systems Confidential
0810_04F7_c2

## Slide 46
Multicast rate limiting
Control the rate at which a sender can send traffic to a group
Input and output rate-limits possible
Source-tree thresholds
For PIM-SM
Switch to SPT tree, if rate exceeds the threshold
Shared tree saves state
Multicast Features:

## Slide 47
Interoperability for different multicast protocols
PIM/DVMRP interoperability
Interaction between PIM SM/DM regions with DVMRP regions
MBONE connection
PIM-SM/PIM-DM interoperability
RP has to be the border router
Multicast Features: Border Router Functionality

## Slide 48
Limitation of Ethernet bridges/switches
Forward all multicast traffic to all ports
Improvements:
IGMP snooping
Data goes to segments with routers and members
Report suppression per segment
CGMP (Cisco Group Management Protocol)
Cisco routers tell switches about router/member segments
Switches do not snoop into IGMP packets
Multicast Features: IP Multicast and Switches

## Slide 49
IP Multicast fastswitching/fastdrop
IP Multicast rate limiting
IP Multicast static routes
mtrace/mrinfo support
PIM NBMA support
PIM SPT thresholding
Cisco Deliverables (11.1)

## Slide 50
Scoped addresses
IGMP v2
CGMP support
Auto-RP
SDR listener support
Helper maps
Cisco Deliverables (11.1)

## Slide 51
11.2F features
PIM over ATM
DVMRP interoperability enhancements
Futures
PIM v2
Performance improvements
Multicast Tag Switching
Cisco Deliverables—11.2F

## Slide 52
http://www.mbone.com
ftp://ftp.cisco.com/ipmulticast.html
ftp://ftp.cisco.com/ipmulticast
Support email:
cs-ipmulticast@cisco.com
MBONE—open session “cisco PIM users”
Release recommended
Stable—11.1(9) New features—11.2 and 11.2F
Documentation